SECTION 08360

SECTIONAL OVERHEAD DOORS

Display hidden notes to specifier by using “Tools”/”Options”/“View”/”Hidden Text” in MS Word 2003 or “Word Options”/”Display”/Hidden Text” in MS Word 2007.

** NOTE TO SPECIFIER **  Amarr Garage Door commercial insulated, non-insulated and aluminum sectional overhead door products.

.

This section is based on the products of Amarr Garage Door, which is located at:

165 Carriage Court

Winston-Salem, NC 27105

Tel: (800) 503-3667

Fax: (336) 251-1851

Email: marketing@amarr.com

www.amarr.com

[click Here] for additional information.

Amarr Garage Doors has been known and respected for its standard of excellence since 1951. Careful attention to detail, the highest quality construction, and unique features are built into every Amarr door. Regardless of model or style, you can be confident that the Amarr door you choose is the finest available and will provide the utmost in security, beauty and value.

Amarr has 69 Door Centers spread throughout the United States, Canada, and Mexico. Each of these Amarr Garage Door Centers are “mini-plants”, stocked with hundreds of sizes and styles of commercial and residential garage doors. In addition, because sometimes you need a door fast, each Door Center can customize doors with options and accessories, to fit most openings – usually within 24 hours.

Amarr Door Centers are staffed with managers who can help you with your day-to-day questions about garage doors, track and springing specifications. This local manager is a reliable source of information for you…when you need it.

Amarr Garage Doors are installed throughout the United States, Canada, and Mexico by professional garage door installers. For the Amarr Door Center nearest you, call our toll free number. We will be happy to direct you to a reliable Amarr Dealer in your area.

SECTION 08360 – SECTIONAL OVERHEAD DOORS

GENERAL

SECTION INCLUDES

** NOTE TO SPECIFIER **  Delete items below not required for project.

Insulated Steel Doors

Track and Framing

RELATED SECTIONS

** NOTE TO SPECIFIER **  Delete any sections below not relevant to this project; add others as required.

Section 04810 - Unit Masonry Assemblies: Prepared opening in masonry.

Section 05500 – Metal Fabrications: - Steel framed door openings.

Section 06100 – Rough Carpentry: Wood framing and blocking for door opening.

Section 07900 - Joint Sealers: Perimeter sealant and backup materials.

Section 08710 - Door Hardware: Cylinder locks.

REFERENCES

** NOTE TO SPECIFIER **  Delete references from the list below that are not actually required by the text of the edited section.

ASTM A 653/A 653M – Specification for Steel Sheet, Zinc-Coated (Galvanized) or Zinc-Iron Alloy-Coated (Galvannealed) by the Hot-Dip Process.

ASTM B 209/209M – Specification for Aluminum and Aluminum-Alloy Sheet and Plate.

ASTM B 221/221M – Specification for Aluminum and Aluminum-Alloy Extruded Bars, Rods, Wire, Profiles and Tubes.

ANSI/DASMA 102-1996.

SUBMITTALS

Submit under provisions of Section 01300.

Product Data:  Manufacturer's data sheets on each product to be used, including:

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Installation methods.

Operation and maintenance data.

Shop Drawings: Include opening dimensions and required tolerances, connection details, anchorage spacing, hardware locations, and installation details.

** NOTE TO SPECIFIER **  Delete selection samples if colors have already been selected.

Selection Samples:  For each finish product specified, two complete sets of color chips representing manufacturer's full range of available colors and patterns.

Verification Samples:  For each finish product specified, two samples, minimum size 6 inches (150 mm) square, representing actual product, color, and patterns.

WIND PERFORMANCE REQUIREMENTS

Design doors to withstand positive and negative wind loads as calculated in accordance with applicable governing building codes.

QUALITY ASSURANCE

Manufacturer Qualifications: Company specializing in manufacturing the types of doors specified in this section with minimum five years documented experience.

Installer Qualifications: Installation to be by qualified dealer in accordance with the manufacturer’s installation instructions.

DELIVERY, STORAGE, AND HANDLING

Store products in manufacturer's unopened packaging until ready for installation.

PROJECT CONDITIONS

Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results.  Do not install products under environmental conditions outside manufacturer's absolute limits.

WARRANTY

Paint finish: 10-year warranty against rust through from cracking, checking or peeling of the paint finish.

Delamination: 10-year warranty against delamination.

PRODUCTS

MANUFACTURERS

Acceptable Manufacturer:  Amarr Garage Doors; 165 Carriage Court, Winston-Salem, NC  27105.  ASD. Tel: (800) 503-3667.  Fax: (336) 251-1851.  Email: marketing@amarr.com   Website: www.amarr.com

** NOTE TO SPECIFIER **  Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

Substitutions:  Not permitted.

Requests for substitutions will be considered in accordance with provisions of Section 01600.

OVERHEAD DOORS - GENERAL

Provide each door with door sections, brackets, tracks, counterbalance mechanisms and hardware to suit the opening and headroom available.

Hardware:

Minimum of 14 gauge galvanized steel hinges and 13 gauge galvanized steel track brackets.

Rollers have 10 ball bearings with casehardened inner and outer races.

Sliding end stile locking device provided with spring-loaded bolt for inside operation only.

Doors 16 feet 4 inches (5102 mm) and wider provided with double end hinges and stiles and long stem rollers.

Tracks: 2 inches (51 mm) or 3 inches (76 mm) as required.

Vertical track 17 or 19-gauge minimum galvanized steel, inclined using adjustable brackets to assure weather tight closure at the jambs.

Horizontal tracks 16-gauge minimum galvanized steel, reinforced with 13 gauge galvanized steel angles as required by door size and weight.

** NOTE TO SPECIFIER **  Select from the following track options; delete options not used.

Provide vertical lift tracks as indicated.

Provide high lift tracks as indicated.

Provide follow roof slope tracks as indicated.

Provide low headroom tracks as indicated.

Spring Counterbalance: Torsion springs for door counter-balance mounted on a continuous cross header shaft. Springs to be oil tempered, helical wound and custom computed for each door. Cable drums to be die cast aluminum. Galvanized lift cable to provide minimum safety factor of five to one. Springs to comply with ANSI/DASMA 102-1996 as follows:

** NOTE TO SPECIFIER **  Select from the following spring cycle options; delete options not used.

Standard Cycle Spring: 10,000 cycles.

High Cycle Spring: 25,000 cycles.

High Cycle Spring: 50,000 cycles.

High Cycle Spring: 100,000 cycles.

Handle: Galvanized steel step plate/lift handle provided on inside and outside of bottom section.

Lock: Standard interior sliding end stile lock with hole to receive padlock.

** NOTE TO SPECIFIER **  Select the following lock option; delete if not used.

Lock: 5 pin cylinder lock interior lock bar and outside key.

Weather stripping: Full length dual contact EPDM rubber bottom seal attached to bottom section.

Weather stripping: Perimeter seal for header and jambs.

** NOTE TO SPECIFIER **  Select one of the following mounting conditions; delete other.

Mounting: Continuous reverse angle mounting for steel jambs.

Mounting: Bracket mounting for wood jambs.

** NOTE TO SPECIFIER **  Select from the following options; delete options not used.

Exhaust port: Installed in bottom sections. Connecting tube from vehicles by others.

INSULATED STEEL DOORS

** NOTE TO SPECIFIER **  Select from the following insulated steel door models; delete models not used.

Model 2700 Commercial 2 inches (51 mm) polyurethane insulated door.

Door Size: As indicated on the Drawings.

Door Sections: 2 inches (51 mm) thick, sandwich construction consisting of rolled formed, commercial quality, 27 gauge exterior and interior steel skins, stucco embossed, and ribbed for added strength. Door to have tongue and groove joint system with EPDM thermal break and weather strip between section joints. Sections to be insulated with CFC free polyurethane, foamed in place by means of a continuous process. . Tested door section R-value of 19.40 is tested in accordance with ASTM C 518-04. Interior skin of each section to have one continuous reinforcing strip, 20 gauge by 3-1/4 inches (83 mm) wide at top and bottom of section to provide mounting of full hinges. End stiles to be 19 gauge standard.

Finish: Door exterior and interior pre-painted steel consisting of a hot dipped galvanized coating applied to the base metal, a 0.2 mil baked on prime coat and an 0.8 mil baked on polyester top coat.

** NOTE TO SPECIFIER **  Select from the following exterior colors; delete colors not used.

Exterior Color: White.

Exterior Color: Brown.

** NOTE TO SPECIFIER **  Select from the following window options; delete options not used.

      - Window Lites: 24 by 6 inches (610 by 152 mm) double insulated acrylic with Black Frame.

Window Lites: 26 by 13 inches (635 by 330 mm) double insulated acrylic with Black Frame.

Thermal Windows/Insulated Glass: 24 by 12 inches (610 by 305 mm) Molded plastic frame with insulated glass. Insulated glass unit to consist of two pieces of 1/8 inch (3.2 mm) thick clear glass with a 7/8 inch (22 mm) aluminum spacer.

Aluminum Fullview Section: Single or dual glazing. Finished with mill finish of 201-R1 clear satin anodized or white powder coat.

FABRICATION

Insulated Steel Doors.

Standard maximum size: Model 2700 32 feet 2 inches wide by 24 feet 1 inch high (9.8m by 7.3m).

Galvanized struts (truss bars): Provide on all doors 12 feet 4 inches (3.8 m) and wider to prevent deflection of no more than 1/120 of the spanned width when in the open position.

EXECUTION

EXAMINATION

Do not begin installation until substrates have been properly prepared.

Verify wall openings are ready to receive work and opening dimensions and tolerances are within specified limits.

PREPARATION

Clean surfaces thoroughly prior to installation.

Prepare opening to permit correct installation of door unit to perimeter air and vapor barrier seal.

INSTALLATION

Install in accordance with manufacturer's instructions. Doors to be interior face mounted on a prepared surface.

Anchor assembly to wall construction and building framing without distortion.

Securely brace door tracks suspended from structure. Secure tracks to structural members or solid backing only.

Fit and align door assembly, tracks and operating hardware.

Install perimeter weatherstripping.

Adjust door assembly to smooth operation and in full contact with weatherstripping.

CLEANING

Clean doors, frames and glass.

Remove labels and visible markings.

PROTECTION

Protect installed products until completion of project.

Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION